Title: Mechanics of concrete and reinforced concrete structures: from material heterogeneities to structural failure with size effect

In this work we address several issues pertaining to efficiency of the computational approach geared towards modeling of inelastic behavior of concrete as a heterogeneous material with microstructure, which is represented by a multiscale model. We elaborate upon the case where the scales remain coupled throughout the computations, implying a constant communication between the finite element models employed at each scale.

We also discuss different manners of representing a complex multi-phase microstructure within the framework of the finite element model constructed at that scale, selecting a model problem of two-phase material where each phase has potentially different inelastic behavior.

The uncertainty aspects are also taken into account pertaining to the incomplete information on the material heterogeneities. The latter is presented as an alternative strategy for bridging the scales, which allows replacing the phenomenological model with random fields for parameters.

Further details can be found in our recent works [1,2,3,4,5,6,7,8,9].

References

[1]	Ibrahimbegovic A., ‘Nonlinear solid mechanics: theoretical formulations and finite element solution methods’, Springer, Berlin, (ISBN 978-90-481-2330), pp. 1-571, (2009)

[2]  Ibrahimbegovic A., B. Brank (eds.), Multi-physicss and multi-scale computer models in nonlinear analysis and optimal design of engineering structures under extreme conditions, IOS Press, Amsterdam, (ISBN 1-58803-479-0)  pp 1-407 (2005)

[3]	Ibrahimbegovic A., J.B. Colliat, M. Hautefeuille, D. Brancherie, S. Melnyk, ‘Probability based size effect representation for failure of civil engineering structures built of heterogeneous materials’, in (eds. M. Papadrakakis et al.), ‘Computational Methods in Stochastic Dynamics’, Springer, Berlin, 289-311, (2011)

[4]   Pham B.H., D. Brancherie, L. Davenne, A. Ibrahimbegovic, ‘Stress-resultant models for ultimate load analysis of reinforced concrete frames and its multi-scale parameter estimates’, Computational Mechanics, 51, 347-360, (2013)

[5]	Niekamp R., D. Markovic, A. Ibrahimbegovic, H. G. Matthies, R.L. Taylor, ‘Multi-scale modeling of heterogeneous structures with inelastic constitutive behavior. Part II : Software coupling and implementation aspects‘, International Journal of Engineering Computations, 26, 6-39 (2009)

[6]  Colliat J.B., M. Hautefeuille, A. Ibrahimbegovic, H.G. Matthies, ‘Stochastic approach to quasi-brittle failure and size effect’, Comptes Rendus de l’Academie des Sciences, Part II: Mécanique, 335, 430-435, (2007)

[7]  Hautefeuille M., J.B. Colliat, A. Ibrahimbegovic, H. Matthies, P. Villon, ‘Multiscale approach to modeling inelastic behavior with softening’, Computer and Structures, 94/95, 83-95, (2012)

[8]  Ibrahimbegovic A., S. Melnyk, ‘Embedded discontinuity finite element method (ED-FEM) versus extended finite element method (X-FEM) for representing the localized failure of heterogeneous materials’, Computational Mechanics, 40, 149-155 (2007)

[9] Dujc J., B. Brank, A. Ibrahimbegovic, ‘Multi-scale computational model for failure analysis of metal frames that includes softening and local buckling’, Computer Methods in Applied Mechanics and Engineering, vol. 199, 1371-1385, (2010)